## Slide 1: A solar system can lose a fifth of its output for days, and nothing tells the owner.
TOMORROW'S SOLAR PLAN · 1 · THE PROBLEM
~22%
below normal for one dusty week
About 540 kWh lost, Feb 10–16
~97%
drop during an inverter fault
Jan 31, 10 hours: 9 kWh made vs ~302 expected
IN THE REAL WORLD
Small solar faults went unnoticed for days or weeks.
Pecan Street study, 2015: "a $5 issue to fix"
Source: our 60-day test data (larger than a typical home), faults added on purpose. Pecan Street, 2015.
Notes: Open with the problem. Our test data: one dusty week cost about 22% of output and a 10-hour inverter fault cut output by about 97%, and nothing raised an alarm. Loss is measured against the Jan 1 to Feb 9 baseline efficiency (our estimate). Public example: a 2015 Pecan Street study found small solar faults went unnoticed for days or weeks (pecanstreet.org/tags/app). We have not interviewed owners, so we do not claim a quote.

## Slide 2: Owners see output after it drops, not what to do next.
2 · THE GAP
What owners face today
Output can drop for days before they notice.
The cause is unclear: dust, a fault, or the weather?
No clear next step, and no sense of what it costs.
Our app, one screen
Outlook: tomorrow's expected output
Check: the problem found, and what kind
Do: what to do about it
Battery: how to use stored power
No login and no dashboard to read. Source for the problem: Pecan Street, 2015.
Notes: The gap: output history tells an owner what already happened. Our app tells them what to expect tomorrow, what is wrong, and what to do, on one screen. Before presenting, if the team has compared specific inverter apps, add what they show and don't show here. We have not verified claims about named apps, so do not make them.

## Slide 3: One screen, three buttons, a plain-language answer.
3 · THE DEMO
Normal day
Check card is green. Nothing is wrong.
Dusty panels
Check card turns orange. Dust (soiling) is flagged.
Inverter fault
Check card turns orange. An equipment fault is flagged.
Try it live
dormathon-modelprototype.streamlit.app
Live demo, no login, simulated data. Random Forest forecast; rules name the cause; ranked by money lost.
Notes: Run the live app: dormathon-modelprototype.streamlit.app. Press Normal day, then Dusty panels, then Inverter fault. Read the actual wording off the screen. Do not read any number aloud unless it matches results/metrics.md or docs/assumptions.md, because the app's built-in fallback numbers are placeholders and it may show dollars while our assumptions use RM. Open the app once before the pitch so it is awake (free Streamlit apps sleep). Keep a screen recording as a backup.

## Slide 4: On test data with faults we added on purpose, the tool found both and named them correctly.
4 · THE PROOF
2 of 2
injected faults caught, with the right type: soiling and equipment fault
54.4% lower forecast error on normal days vs "same hour yesterday"
46.9% lower on the fault scenario
Worse on the dusty scenario (we say so)
1 false alarm on clean data
Robust: fault still caught with noise and 5% of rows dropped
Source: results/metrics.md. Data: 60 days of hourly readings, Jan 1 to Mar 1, 2026, with faults added on purpose.
Notes: Both injected faults were caught with the right type, with 1 false alarm on clean data, and the fault was still caught with noise added and 5% of rows dropped. Forecast error was 54.4% lower than "same hour yesterday" on normal days and 46.9% lower on the fault scenario, but worse on the dusty scenario. Say so if asked. This is test data, not proof on real homes: the next step is real data. Confirm results/metrics.md is final and whether the data is simulated before presenting.

## Slide 5: The app tells an owner when dust is worth cleaning, and catches faults that cost far more.
5 · IMPACT AND NEXT STEPS
~60 days
of 22% dust loss before one RM 150 cleaning pays for itself
A fault costs about RM 154 over 14 days
Assumed example home: 4.7 kWp, 25.7 kWh/day, RM 0.44/kWh, 14 days earlier detection.
Next steps
1. Test on real homes with real inverter data
2. Improve the forecast on dusty days
3. Add more problem types and send the message to the owner's phone
Not built on purpose: login, generic dashboard, live inverter connection, mobile app, notifications.
Jun Xi · Hong Jun · Cheng Hao | dormathon-modelprototype.streamlit.app
Notes: Say "assumed" out loud for every RM figure. Loss per day = daily output x dust loss x tariff. For an example 4.7 kWp home (25.7 kWh/day, RM 0.44/kWh from the 2025 TNB tariff): a short dusty spell costs less than one cleaning, so the app does not say rush out and clean. It says when dust has lasted long enough to be worth cleaning (about 60 days at our 22% test loss, about 265 days at a typical 5%), and it catches faults that cost about RM 154 over 14 days (97% loss). Sources and inputs are in docs/assumptions.md; all inputs are TO CONFIRM. The next steps are our suggestions: edit them to match what the team plans. Close: Tomorrow's Solar Plan tells a homeowner what to expect tomorrow, what is going wrong, and what to do.